## Slide 1
VERILOG HDL • RTL DESIGN & VERIFICATION
1 × 3 Packet Router
A synchronous router that steers byte-stream packets from one input to three output channels — designed and verified from scratch in Verilog.
FSM Controller
16×9 FIFOs ×3
Parity Check
Soft-Reset Timeout
Chaitanya Roy | Interview Preparation Deck

## Slide 2
THE BIG PICTURE
What have I built?
2
In one line
A 1-to-3 packet router: it reads a stream of bytes on one input port, looks at the address in the packet header, and delivers the packet to one of three output channels — while checking it for errors.
Think of it as a tiny post office
Letters (bytes) arrive at one counter. The clerk reads the address on the envelope, drops each letter into the right mailbox (FIFO), and a parity check makes sure nothing was corrupted on the way.
1 input → 3 outputs
data_in
8-bit
ROUTER
out_0
out_1
out_2
Address bits [1:0] pick the channel: 00→0 01→1 10→2

## Slide 3
THE DATA
The packet format
3
Every packet is a stream of bytes with three parts. The very first byte is the header — it tells the router where to go and how big the packet is.
HEADER
1 byte
addr[1:0] + length[7:2]
PAYLOAD
1–63 bytes
the actual data
PARITY
1 byte
error-check byte
Inside the header byte
bit 7
bit 6
bit 5
bit 4
bit 3
bit 2
bit 1
bit 0
length [7:2] — how many payload bytes
addr [1:0] — destination channel

## Slide 4
ARCHITECTURE
Five blocks working together
4
router_top just wires these five sub-modules together — no logic of its own (structural design).
router_reg
Builds the datapath byte:
parity gen + error check
router_fsm
The brain — 8-state
controller, all timing
router_sync
Routes write enables +
soft-reset timeout
FIFO_0
16×9 buffer
channel 0
FIFO_1
16×9 buffer
channel 1
FIFO_2
16×9 buffer
channel 2
dout (data)
write_enb
The FSM sits in the middle and controls both the register (what byte to build) and the synchronizer (which FIFO to write). The three FIFOs buffer data until each output channel reads it.

## Slide 5
DATAFLOW
How a packet travels through
5
1
Header arrives
pkt_valid goes high; FSM reads addr[1:0] to pick the channel and checks that FIFO is empty.
2
Latch & route
router_reg captures the first byte; router_sync asserts write_enb for the chosen FIFO only.
3
Stream payload
Each clock, a payload byte flows through dout into the FIFO. Parity is XOR-accumulated as it goes.
4
Check parity
Last byte is the packet's parity. FSM compares it to the internal parity → error flag.
5
Read out
valid_out goes high; the destination pulls bytes out with read_enb. FIFO empties, back to idle.

## Slide 6
FSM DEEP-DIVE
The 8-state controller
6
Two always blocks for state (sequential present-state + combinational next-state), one for outputs. Every control signal in the whole router is generated here.
0
DECODE_ADDRESS
Idle. Read addr, wait for a valid packet.
1
LOAD_FIRST_DATA
Latch header byte into the register.
2
LOAD_DATA
Stream payload bytes into the FIFO.
3
LOAD_PARITY
Capture the incoming parity byte.
4
CHECK_PARITY_ERROR
Compare parity → set error flag.
5
FIFO_FULL_STATE
FIFO full — stall, hold the byte.
6
LOAD_AFTER_FULL
Resume once FIFO has space again.
7
WAIT_TILL_EMPTY
Target busy — wait until it drains.

## Slide 7
FSM DEEP-DIVE
Normal packet flow + branches
7
DECODE
ADDRESS
LOAD_FIRST
DATA
LOAD
DATA
LOAD
PARITY
CHECK_PARITY
ERROR
→ back to DECODE_ADDRESS for the next packet
Branch: FIFO fills up mid-packet
LOAD_DATA → FIFO_FULL_STATE → LOAD_AFTER_FULL
The byte that couldn't be written is parked in an internal register (full_state_byte) and pushed in the moment space frees up — no data lost.
Branch: target channel is busy
DECODE_ADDRESS → WAIT_TILL_EMPTY
If the addressed FIFO isn't empty, the FSM waits there until the previous packet is fully read, then starts loading — prevents mixing two packets in one FIFO.

## Slide 8
DATAPATH
router_reg — parity & error
8
This block builds the byte that goes to the FIFO and does the packet's error checking.
1
Byte assembly
Drives dout: header first, then each payload byte. If the FIFO is full it stashes the byte in full_state_byte instead of losing it.
2
Parity generation
XOR-accumulates every header + payload byte into internal_parity as the packet streams through.
3
Parity capture
When the packet ends, the incoming parity byte is captured into pkt_parity.
4
Error detection
If pkt_parity ≠ internal_parity once parity_done is set → err = 1. Otherwise the packet is clean.

## Slide 9
DATAPATH
router_fifo — the 16×9 buffer
9
Why 9 bits wide, not 8?
Each location stores 9 bits = { lfd_state , data[7:0] }. The extra top bit marks the first byte (header) of a packet, so the read side knows where each packet begins and can recover its length.
Pointers & flags
• 5-bit read/write pointers (4 addr bits + 1 wrap bit) • empty when wr_ptr == rd_ptr • full when the wrap bits differ but addresses match • Reads/writes guarded to prevent under/overflow • Down-counter drives data_out to high-Z after the packet is fully read
16 locations × 9 bits
lfd=1 header
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
0 payload
Top bit (lfd) = 1 only on the first byte

## Slide 10
DATAPATH
router_sync — routing & timeout
10
1
Write-enable routing
Decodes the latched address and asserts exactly one of write_enb[2:0], so a packet is written to only its target FIFO.
2
valid_out signals
Drives valid_out_x = ~empty_x, telling each channel when its FIFO holds data ready to be read.
3
fifo_full mux
Selects the full flag of the active FIFO and feeds it back to the FSM as fifo_full.
4
Soft-reset timeout
One counter per channel. If a channel has data but isn't read for 30 clocks, it raises soft_reset — clearing a stuck FIFO so the router never deadlocks.

## Slide 11
THE 'WHY'
Design decisions a senior will probe
11
9-bit FIFO word
The 9th bit tags the header byte so packet boundaries survive inside the FIFO.
Separate FSM
One central controller = clean, timing-safe control; datapath blocks stay simple and reusable.
Store-on-full, not drop
full_state_byte holds the stalled byte so a full FIFO never loses data.
Parity by XOR
Cheap 1-byte checksum; accumulate on write, compare at end — minimal hardware.
30-cycle soft reset
A dead channel self-heals instead of blocking the router forever (livelock guard).
busy handshake
Tells the source to pause while the FSM is mid-packet — simple flow control.

## Slide 12
VERIFICATION
How I tested it in Verilog
12
Every module has its own testbench (tb/), plus a top-level testbench that drives a full 14-byte packet end-to-end.
1
Reusable tasks
initialise, rst_dut and stimulus tasks keep each testbench clean and readable.
2
Scenario-driven
FSM tb walks named scenarios (s1, s2…) that hit every state path — normal, FIFO-full, wait-till-empty.
3
Directed packets
Top tb builds a header + payload + parity stream with a for-loop and pulses read_enb to drain the FIFO.
4
Waveform check
$dumpfile / $dumpvars generate .vcd files (viewed in GTKWave) to confirm signals cycle-by-cycle.
5
Per-block sign-off
FIFO, register, sync and FSM each verified in isolation before integrating in router_top.
6
Parity both ways
Tested clean packets (err=0) and corrupted parity (err=1) to prove error detection works.

## Slide 13
REAL ENGINEERING
Problems I hit & how I solved them
13
Problem: Data lost when FIFO filled mid-packet
Fix: Added the FIFO_FULL / LOAD_AFTER_FULL states and a full_state_byte register that parks the stalled byte and re-injects it when space opens up.
Problem: Two packets landing in one FIFO
Fix: Introduced WAIT_TILL_EMPTY: the FSM holds until the target channel is fully drained before it starts a new packet.
Problem: A slow reader blocking the router forever
Fix: Built the 30-clock soft-reset counter in the synchronizer so an unread channel resets itself — no permanent deadlock.
Problem: Losing packet boundaries inside the FIFO
Fix: Widened the FIFO to 9 bits and tagged the header byte with lfd_state so length is recoverable on read-out.
Problem: Accidental latches in next-state logic
Fix: Used a default assignment + always @(*) with a full case so every branch is defined — clean synthesis, no latches.

## Slide 14
IN ONE BREATH
What to say when they ask
“Tell me about your project”
“I designed and verified a synchronous 1×3 packet router in Verilog. It reads a byte-stream packet, decodes the destination from the header, buffers the payload in one of three 16×9 FIFOs, and validates it with a parity check. A single 8-state FSM drives all control — including graceful handling of FIFO-full, busy channels, and a soft-reset timeout so it never deadlocks. I verified each block with its own scenario-based testbench and the full router end-to-end using waveforms.”
Synchronous RTL
FSM control
FIFO buffering
Parity check
Self-healing timeout